## Slide 1: Algebraic Analysis and Design of Routing Protocols
João Luís Sobrinho
Instituto Superior Técnico, Universidade de Lisboa
Instituto de Telecomunicações
IETF-111

## Slide 2: Outline
Algebraic approach to routing
Analysis: from routing protocols to routing problems
Design: from routing problems to routing protocols
Final remarks

## Slide 3: Early networks: shortest paths
[Schwartz & Stern 1980]
Distance-vector
& link-state routing protocols
Shortest path routing
1. Algebraic approach to routing
Notes: Dijkstra and Bellman-Ford algorithms were well-known by the time shortest-path routing protocols were invented.
In the case of non-restarting distance vector protocols, there the problem of count-to-infinity had to be dealt with.

## Slide 4: A variety of networks: non-shortest paths
Context | Routing | Protocol | Behavior
Quality-of-service | Delay and bandwidth | EIGRP | Sub-optimal paths
Internet | Decentralized policies | BGP | Oscillations
Interconnection | Distinct routing instances | AD & RR | Forwarding loops
Wireless | Generic metrics | old Babel | Black holes
[Varadhan et al. 2000, Griffin et al. 2002, Gouda & Schneider 2003, Le et al. 2008, Sobrinho 2019]
1. Algebraic approach to routing
Notes: Old Babel is RF 6126 from 2011; recent babel is RFC 8966 from 2021. The difference is in section 3.6 “Route selection”.
New protocols are not shortest-path routing protocols.

## Slide 5: Routing problems or routing protocols?
Distance-vector
& link-state routing protocols
Non-shortest path routing protocol
(BGP, EIGRP, AD & RR, old Babel, etc.)
What is the routing problem being solved?
What guarantees correct behavior?
Shortest path routing
1. Algebraic approach to routing
Notes: The development of non-shortest path routing protocols was somewhat ad hoc by adaptation of operation rules of distance vector protocols oftentimes without full comprehension of the global behaviors induced by those adaptations
Sweeping away undesirable behaviors, what is the problem that a non-shortest-path routing protocol is attempting to solve?

## Slide 6: Routing algebras
Attributes : context-specific metrics and/or policy decisions
Total order :
Extension operation :
Algebraic entwinement of total order and extension operation determines behaviors of a routing protocol
1. Algebraic approach to routing
Notes: Difficulty may be recognizing the attributes, total order, and extension operation underlying a non-shortest path routing protocol.
Most routing protocols are generalizations of distance-vector protocols rather than of link-state protocols.

## Slide 7: Shortest paths
Attributes: length,
Total order:
Extension operation:
1. Algebraic approach to routing
Notes: 1. Description in common terms with a mathematical substance

## Slide 8: Widest paths
Attributes: width,
Total order:
Extension operation:
1. Algebraic approach to routing

## Slide 9: Shortest-widest paths
Attributes: (width, length),
Total order:
Extension operation:
[Wang & Crowcroft 1996]
The composite metric of EIGRP generalizes this total order
1. Algebraic approach to routing
Notes: 1. Description in common terms with a mathematical substance

## Slide 10: Minimum energy paths
Attributes: (energy, success probability):
Total order:
Extension operation:
[Dong et al. 2005]
End-to-end rather than hop-by-hop retransmissions
1. Algebraic approach to routing
Notes: 1. Description in common terms with a mathematical substance

## Slide 11: Best type-of-relationship paths
Attributes: Type-of-Relationship (ToR),
Total order:
Extension operation:
[Gao & Rexford, 2001]
Every intermediate node along a path must profit from transiting traffic
1. Algebraic approach to routing
Notes: Algebraic formulation of policies at least as they are implemented with BGP. No exportation or importation leads to invalid paths; ranking leads to total order.
Peer routes do not have to be preferred to peer routes

## Slide 12: Outline
Algebraic approach to routing
Analysis: from routing protocols to routing problems
Design: from routing problems to routing protocols
Final remarks

## Slide 13: Example: shortest-widest paths
Pairs (width, length):
Shortest-widest order: preferred to if
Product extension: extended with is
2. Analysis: from protocols to problems
Preference
Preference

## Slide 14: Vectoring protocol I
(width, length): next.hop
Elected (width, length) in bold
2. Analysis: from protocols to problems

## Slide 15: Vectoring protocol II
(width, length): next.hop
Elected (width, length) in bold
2. Analysis: from protocols to problems

## Slide 16: Vectoring protocol III
(width, length): next.hop
Elected (width, length) in bold
2. Analysis: from protocols to problems

## Slide 17: Sub-shortest-widest path routing
(width, length): next.hop
data-packets
Elected (width, length) in bold
Data-packets are not forwarded along shortest-widest paths
2. Analysis: from protocols to problems

## Slide 18: Understanding sub-optimality
Extension inverts the relative preference between two pairs (width, length)
2. Analysis: from protocols to problems
Extension
with
Elected
Preference
Elected
Not visible
Hidden
Preference

## Slide 19: Left-isotonicity
for all attributes
Extension preserves the relative preference between two attributes
Left-isotonicity
2. Analysis: from protocols to problems
Notes: 1. In the case of vectoring protocols, left-isotonicity implies the na atribute that a node hides from a neighbor is of no interest to the neighbor.

## Slide 20: Vectoring protocols under left-isotonicity
Optimal path routing
left-isotonicity,
strictly left-inflationary cycles
But: left-isotonicity does not hold in many practical cases
Vectoring protocols
(BGP, EIGRP, AD & RR, etc.)
2. Analysis: from protocols to problems

## Slide 21: The problem solved by vectoring protocols
Optimal destination-based routing
strictly left-absorbent cycles
Strict left-absorbency is stronger than strict left-inflation but weaker than the combination of strict left-inflation and left-isotonicity [Sobrinho 2016]
2. Analysis: from protocols to problems
Vectoring protocols
(BGP, EIGRP, AD & RR, etc.)

## Slide 22: Outline
Algebraic approach to routing
Analysis: from routing protocols to routing problems
Design: from routing problems to routing protocols
Final remarks

## Slide 23: Overcoming sub-optimality
What is the smallest set of attributes that must be elected to contain the optimal attributes?
If elects both and , then does learn
3. Design: from problems to protocols
Elected (width, length) in bold
(width, length): next.hop

## Slide 24: Left-isotonic reduction
Reduction: is contained in
Left-isotonicity: is left-isotone for
Partial order is a left-isotonic reduction of
  [Lengauer & Theune 1991, Sobrinho & Ferreira 2020]
Every order has a largest left-isotonic reduction
3. Design: from problems to protocols
Attributes and are incomparable in
Neither nor

## Slide 25: Example: shortest-widest order
3. Design: from problems to protocols
Incomparable
Less preferred
Width
Length
Preferred
Less preferred
Width
Length
Incomparable
Shortest-widest order
Product order on pairs (width, length)
Preferred
Largest
left-isotonic
reduction

## Slide 26: Partial-order vectoring protocol I
3. Design: from problems to protocols

## Slide 27: Partial-order vectoring protocol II
(width, length), label: next.hop
Locally unique labels distinguish elected pairs (width, length)
3. Design: from problems to protocols
Elected (width, length) in bold

## Slide 28: Partial-order vectoring protocol III
(width, length), label: next.hop; next.label
Labels propagated alongside pairs (width, length)
3. Design: from problems to protocols
Elected (width, length) in bold

## Slide 29: Shortest-widest-path routing
2
labeled data-packets
Data-packets are forwarded along shortest-widest paths
(width, length), label: next.hop; next.label
2
3. Design: from problems to protocols
Elected (width, length) in bold

## Slide 30: Future networks: specification of routing paths?
Partial-order vectoring protocol
Optimal path routing
strictly left-inflationary cycles
Partial-order is the largest left-isotonic reduction of the total order
  [Sobrinho & Ferreira 2020]
3. Design: from problems to protocols
Notes: Although I presented a running example concerning shortest-widest paths, the implications of isotonicity to inter-AS routing has additional insights concerning the relationship between individual incentives and social welfare. Left-isotonicity implies that what is best for me is best for may neighbor. When we want to upgrade the inter-AS routing system from a global state A to a global state B in the presence of left-isotonicity AS have local incentives to do their part in the direction of B

## Slide 31: Final remarks
Insight into the operation of routing protocols
Unified analysis of routing protocols; not just vectoring protocols
Principled design of routing protocols; not just optimality problems
Notes: Other protocols: restarting vectoring protocols.
Multiple optimality criteria; constraints on paths such as going through a chain of services; optimal path with na approximation tolerance.
BGP policies can be formulated an optimal path problema.

## Slide 32: Example: shortest-best-ToR paths
Pairs (ToR, hop-count):
Shortest-best-ToR order: preferred to if
Product extension: extended with is if ; otherwise, is
Preference
Preference

## Slide 33: BGP
(ToR, hop-count): next.hop
Elected (ToR, hop-count) in bold
Data-packets are not forwarded along shortest-best-ToR paths
data-packets

## Slide 34: No left-isotonicity
Preference
Preference
Extension
with
Elected
Elected
Not visible
Hidden

## Slide 35: Partial-order BGP
(ToR, hop-count), in_links: next.hop
Elected (ToR, hop-count) in bold
Data-packets are forwarded along shortest-best-ToR paths
data-packets
Forwarding as a function of incoming links; labels not required

## Slide 36: Deployment and incentives
Stub ASes run BGP
ISPs have local incentives to adopt partial-order BGP
By offering to AS , AS transits its traffic to AS : local incentives are aligned with social optimum thanks to left-isotonicity!