## Slide 1: The Extensible Internet (EI)
Based on a CCR editorial with 18 authors:
Hari Balakrishnan, Sujata Banerjee, Israel Cidon, David Culler, Deborah Estrin, Ethan Katz-Bassett, Arvind Krishnamurthy, James McCauley, Nick McKeown, Aurojit Panda, Sylvia Ratnasamy, Jennifer Rexford, Michael Schapira, Scott Shenker, Ion Stoica, David Tennenhouse, Amin Vahdat, Ellen Zegura
Core design team: Arvind Krishnamurthy (UW), James McCauley (MHC), Aurojit Panda (NYU), Scott Shenker

## Slide 2: Enabling Architectural Change?
In this talk, “architecture” refers to overall arrangement of dataplane functionality
  Arch. = Layers and their basic functions
  Not specific protocols (e.g. IPv4 vs IPv6)
  Not control plane (e.g., SDN, etc)
Decades of architectural research...
  ...but no discernable architectural impact
Why not?
  Did not identify the key deployment challenge
  That challenge arises in L3

## Slide 3: L3 Has Two Roles in Architecture
Allows all L2 networks to interconnect
  Must be deployed in every router
  Almost impossible to make significant change
    Both now, and in the future...
Provides the service model to hosts
  i.e., IP’s best effort packet delivery
  Must support all application requirements
    From content/streaming to AR/VR, gaming, IoT...
  Requirements becoming more stringent
    Latency, reliability, privacy, security,...

## Slide 4: A Fundamental Paradox
We must redesign the network to meet a wider range of application requirements without changing IP
How can we do this?

## Slide 5: Lessons from CCPs
Cloud/content providers building private IP-based networks with many PoPs
These PoPs apply in-network services:
  Flow termination
  Caching
  Load balancing
  ...
Services designed to meet app rqmts

## Slide 6: Good for Apps, Bad for Internet
Internet increasingly balkanized
  Private nets define own in-network services
  Public Internet lagging behind
Rather than these ad hoc and proprietary designs, we need a coherent architecture
  Support broader set of in-network services
  Become the new Internet service model
EI is nothing more than the architecturally coherent form of these private networks

## Slide 7: The Extensible Internet (EI)
Basic Design
Example Services

## Slide 8: Core Design Is Very Simple
Use current IP protocol/infrastructure
  Remains essentially unchanged
Introduce a new network layer above L3
  Service layer (SL) or L3.5
SL offers new in-network services to hosts
  Like the current private nets, but more general

## Slide 9: EI Decouples L3’s Two Roles
Current L3 is the interface to both
  L2 networks: so it must be narrow waist
  L4 on hosts: defining Internet’s service model
In EI
  L3 is still the interface to L2 networks
  But L3.5 is the interface to L4
No reason for L3.5 to be “narrow”
  So it can meet a wide range of needs
Nor any reason to be in every router
  So it can be more easily deployed/changed

## Slide 10: The Service Layer (SL)
Implemented at service nodes (SNs)
  SNs are servers deployed at network “edge”
  Every host associated with a service node
  SL also implemented at hosts (like all layers)
Typical communication pattern:
  Source → SN → SN → Destination
  Service layer communication tunneled over IP
  Source specifies which service to invoke at SN
    So services need not be backwards-compatible

## Slide 12: Key: All Services In Software
Standards: Open-source code, not specs
Necessary software pieces on SNs
  Standardized service modules
  Standardized execution environment (WORA)
  Open-source runtime/orchestration available
Services involve limited computation
  Packet forwarding and payload processing
  Simple functions like caching
SNs could have enclaves, hw accelerators

## Slide 13: Choosing The Services
Governance process determines the set of public services and their implementations
  Public services are deployed in all SNs
  Form the new Internet service model
  Service model is easily extensible
EI’s biggest change: deployment model
  Services are approved software modules
  Easily deployable in all SNs (WORA)
  No per-vendor/per-domain decision process

## Slide 14: Interdomain Routing in SL
In the SL, packets travel directly between source and destination domains
  Peering at SL is direct and settlement-free
  Necessary for network neutrality, etc.
The actual L3 transit between SNs in different domains can be via
  Normal L3 routing (with SL tunneled on top)
  Using an IXP as an intermediary
  Leased or private lines between the SNs
  ….

## Slide 15: Isn’t EI Just An Overlay?
Yes, of course it is an overlay!
  The layered Internet architecture is nothing but a structured set of intrinsic overlays
  L4 overlay on L3; L3 overlay on L2; L2 overlay on L1
  Dictates the what and where of each layer
EI: structured, intrinsic overlay dictating:
  Where it fits in the layering scheme (L3.5)
  Where it is implemented (SNs)
  How the overlay fits into the domain structure
    Peering, payments, etc.

## Slide 16: Examples of EI Services

## Slide 17: EI: Expanded Packet Delivery
Basics:
  Best-effort packet delivery (IP+)
  Flow termination
  Caching
  Load balancing
  Redirection
New delivery models:
  Pub/Sub and Anycast
  Information-centric networking (ICN)

## Slide 18: EI: Supporting Emerging Use Cases
AR/VR/gaming
  Pub/sub to local users
  Aggregation/compression to backend
Autonomous Vehicles:
  Pub/sub, local queries, caching, redirection
IoT:
  Aggregation/compression, simple queries

## Slide 19: EI: Security and Privacy
Use enclaves to secure SN state/software
Attestation
  Ensure clients connect to SN-verified servers
Privacy:
  oDNS-like name lookups and Tor-like delivery
DDoS protection
  SNs support “shut up” messages

## Slide 20: But this is just the beginning...
EI is an extensible and evolvable platform
More services will be added as needed...

## Slide 21: Current Status and Future Plans

## Slide 22: Development Status
Initial infrastructure ready by mid-August
Will start with deployment on FABRIC
  Then other testbeds and clouds (credits)
Will hold community workshops
  On services, apps, infrastructure
We will need everyone’s help
  Financial, intellectual, organizational, code
  If interested in helping, please contact me (shenker@icsi.berkeley.edu)

## Slide 23: How Can This Become Reality?
Stage 1: EI as Experimental Platform
  Deployed on testbeds, clouds (credits)
  Research on services, apps, infrastructure
Stage 2: Critical Transitional Phase
  EI reliable enough for some widely-used apps
  Ecosystem can see potential benefit
  Clouds and others begin serious support
Stage 3: Carrier Adoption Begins
  Carriers see opportunity, and threat
  Can deploy without change to rest of infra.
    Already tested in production
    Can use Edge Computing resources

## Slide 24: EI Based On Simple Conjecture
That in-network support for applications:
  Is important for many current/emerging apps
  Can be done at SNs, rather than each router
  Can be done in software, not ASICs
Evidence for conjecture: private networks
  EI is merely the architecturally coherent version of these private networks
That’s why we think EI might succeed...

## Slide 25: Thank You For Your Attention!
Questions?